## Slide 1: Huffman Encoding
Based on Hardware

## Slide 2: Outline
Introduction
Encoder Implementation
Algorithmic State Machine
Software to Hardware Conversion
Results
Motivation

## Slide 3: Motivation
Storage
Wireless
Less traffic means
Less Power Consumption
Zip(Deflate) compression is widely used!
More storage with
No Extra Cost
The Zip hardware implementation is quite promising
ZIP
Fast enough for real-time processing

## Slide 4: Motivation
Zip Encoder Workflow
Merge the duplicated Strings
LZ77
Huffman
Tree_Sorter
Tree_Constructor
Tree_Encoder
Raw Data
Input
Compressed Data
Output

## Slide 5: Introduction
1. Find two nodes with minimum weights
2. Add these two weights, the result of which is inserted into table as a new node. And then remove the previous two nodes
3. Go to step 1, until there is only one node in the table
Build a Huffman Tree
Huffman Tree
Text Input
Char | Weight
a | 1
c | 3
g | 2
d | 5
m | 4
… | 0
… | 0
Char | Weight
c | 3
d | 5
m | 4
(a, g) | 3
… | 0
a
g
3
2
1

## Slide 6: Introduction
Huffman Encoding
Char | Weight
a | 1
c | 3
g | 2
d | 5
m | 4
… | 0
… | 0
From up to down, Left node is marked as ‘0’, and Right node is marked as ‘1’
The encoded data cannot be the prefix of the other encoded data.
Encoding Procedure
a
g
3
2
1
c
6
3
m
10
4
d
15
5
0
1
0
1
0
1
0
1
g: 001
Char | Weight
a | 000
c | 01
g | 001
d | 11
m | 10
1000001
m a c
3*8bits -> 7 bits
Save 17 bits!!

## Slide 7: Implementation
Design Methodology
Software Simulation
Algorithmic State Machine Design
Hardware Implementation
Apply the ASM design methodology to convert the algorithm to hardware.
Simulate the algorithm in C language/ Pseudo code. Thinking in a “Hardware” way.
Implement the designed RTL architecture from the previous step in HDL. And then verify the hardware module(s).

## Slide 8: Software Simulation
Design Methodology
Tree_Sorter
Tree_Constructor
Tree_Encoder
Code_Dumper
Main
State Machine Controller
Key Components
IDE: Dev C++ Compiler: gcc
Tree_Constructor: Build the Huffman tree from heap by calling Tree_Sorter
Tree_Sorter: Return two nodes with the minimum weights
Tree_Encoder: Encode the Huffman tree to binary code

## Slide 9: ASM
Design Methodology
Convert the pseudo code into an ASM chart
 Create a data path based on the ASM chart
 Design the control logic based on the detailed ASM chart
Let’s take Tree_Sorter as an example.
Array Transformation
Address | Char[7:0] | Weight[7:0] | HuffmanCode[7:0]
0 | ‘a’ | 1 | 0
Code_RAM
Tree_RAM
Address | Weight[7:0] | LC[7:0] | RC[7:0] | Parent[8:0]
0 | 3 | 1 | 2 | -1

## Slide 10: Hardware Implementation
ASM Chart
Convert the code into an ASM chart

## Slide 11: Hardware Implementation
Datapath
Create a data path based on the ASM chart

## Slide 12: Hardware Implementation
Control Logic
Design the control logic based on the detailed ASM chart

## Slide 13: Hardware Implementation
Verification
Address | Weight | LC | RC | Parent
0 | 18 | -1 | -1 | -1
1 | 67 | -1 | -1 | -1
2 | 6 | -1 | -1 | -1
3 | 1 | -1 | -1 | -1
4 | 10 | -1 | -1 | -1
5 | 34 | -1 | -1 | -1
6 | 3 | -1 | -1 | -1
Tree_RAM

## Slide 14: Results
ASM Design
Hardware Implementation
Tree_Constructor, Tree_Sorter, and Tree_Encoder
Tree_Sorter
Name | Number
Combinational ALUTS | 78/12,480
Dedicated Logic registers | 66/12,480
Total block memory bits | 17920/419,328
Synthesis Result
Tree_Sorter (Quartus 8.0), Altera Stratix II Board

## Slide 15: Thank You!
Any Questions?